## Slide 1
PROGRAM : COMPUTER ENGINEERING
SEM : I
YEAR : 1ST
COURSE : ENGINEERING GRAPHICS
COURSE CODE : ENG198904
NAME OF THE FACULTY: SHARYU R. KADAM

## Slide 2: CO’S

## Slide 5: CH- 1 Drawing Instruments and their uses

## Slide 6: Engineering Drawing
Technical drawing

## Slide 7: Engineering Drawing
Graphical Language
Exchange Information

## Slide 8
Artistic Drawing
Engineering Drawing
?
Why this banyan tree drawing is not engineering drawing ?

## Slide 9
Engineering is the profession in which a knowledge of mathematical and natural science gained by study, experience and practice is applied with judgment to develop product.
Although the works of artists (or photography and other method of reproduction) may provide pictorial representation, but they cannot serve as engineering description.

## Slide 11
Applications of Engineering Graphics :
Ships

## Slide 12
Applications of Engineering Graphics :
Automobiles :

## Slide 13
Applications of Engineering Graphics :
Construction :

## Slide 14
Drawing Board

## Slide 16
Drafter

## Slide 19
Drawing Sheet

## Slide 25
IPv6

## Slide 27
IPv6

## Slide 31
A scale is defined as the ratio of the linear dimensions of the object as represented in a drawing to the actual dimensions of the same.
SCALES :
Some objects like buildings, machines etc are big
some objects are very small like parts used in wrist watches
Some Drawing of above is required to be drawn proportionally reduced or enlarged.
The proportion by which we are enlarging or reducing actual length of the object on drawing is called as scale.

## Slide 32
Scale Size :
Full size.
Reduced size.
Enlarged size.

## Slide 33: 1. Full size
4 cm
5 cm
5 cm
4 cm
The scale in which objects are drawn with actual measurement is called as full size scale.
It is written in ration 1:1

## Slide 34: 2. Reduced size
2 cm
2.5 cm
5 cm
4 cm
The scale in which objects are drawn with reduced proportion is called as reduced size scale.
It is written in ration 1:2 , 1:5, 1:10, 1:20

## Slide 35: 2. Enlarged size
2 cm
2.5 cm
5 cm
4 cm
The scale in which objects are drawn with increased proportion is called as reduced size scale.
It is written in ration 2:1 , 5:1, 10:1, 20:1

## Slide 36: Representative Fraction (R.F.)
It is ration of the length of the object on the drawing to the actual length of the object
R.F.
=
Length of object on the drawing
Actual length of object

## Slide 37: 1. Full size
4 cm
5 cm
5 cm
4 cm
The scale in which objects are drawn with actual measurement is called as full size scale.
It is written in ration 1:1
R.F.
=
1

## Slide 38: 2. Reduced size
2 cm
2.5 cm
5 cm
4 cm
The scale in which objects are drawn with reduced proportion is called as reduced size scale.
It is written in ration 1:2 , 1:5, 1:10, 1:20
R.F.
<
1

## Slide 39: 2. Enlarged size
2 cm
2.5 cm
5 cm
4 cm
The scale in which objects are drawn with increased proportion is called as reduced size scale.
It is written in ration 2:1 , 5:1, 10:1, 20:1
R.F.
>
1

## Slide 40
Type Of Scale :
Plain Scale.
Diagonal Scale.

## Slide 41
Metric Measurements:
1 cm | = | 10 mm
1 dm | = | 10 cm
1 m | = | 10 dm
1 dam | = | 10 m
1 hm | = | 10 dam
1 km | = | 10 hm
1 Yard | = | 3 Feets
1 feet | = | 12 inches
1 inch | = | 2.54 cm
mm | = | Millimeter
cm | = | centimeter
dm | = | decimeter
m | = | meter
dam | = | decameter
hm | = | hectometer
km | = | kilometer
Note : Always calculate in cm

## Slide 42: Plain Scale
This scale is used when very small distances are to be accurately measured for example 0.1 mm
When measurements are required up to one decimal place (i.e. 2 unit)
Example : 6.7 , 5.3
6.7 m
6 meter & 7 decimeter
2.3 cm
2 cm & 3 mm
For constructing plain scale we must know:
Its representative fraction i.e. (R.F.) (given or calculate)
Maximum length to be measured (given)
The units to be shown, for example, milimeters and centimeters(given)

## Slide 43
Steps for constructing plain scale
1. Calculate the length of scale.
length of scale = R.F X length to measured
2. Draw two horizontal lines parallel to each other and some distance apart so that they give appearance as a rule. Join the ends by vertical lines.
(1. Length for horizontal parallel lines = length of scale which is calculated previously 2. assume suitable length)
3. Divide horizontal lines into required number of equal parts and ( depend upon length to measured or read upto)
4. draw perpendicular lines at these division points.
5. Mark ‘zero’ at the end of first division.
0
1
2
3
4
6. sub-divide only first main part to the left of zero into the required number of sub-division according to unit.
Example : 3.2 m means 3 meter and 2 decimeter
decimeter
meter
1 m = 10 decimeter
Hence we need to divide first part into 10 equal numbers
7. Sub-divisions are numbered to the right, starting from zero.
1
2
3
10
8. Mark the given distance on scale
9. name of the scale and R.F. should be mentioned below scale
PLANE SCALE
R.F. =
Mark Distance

## Slide 44
Problem 1 :
Construct a plain scale with R.F. 1:40 to read up to 5 meters in meters and decimeters. Mark 3.4 m on scale
1. Calculate the length of scale.
length of scale = R.F X length to measured
= 1/40 X 5 m
= 0.125 m
= 0.125 X 100 = 12.5 cm
Given data : R.F. = 1/40 , maximum length = 5 m
2. Draw two horizontal lines of 12.5 cm parallel to each other and 2 cm distance apart. Join the ends by vertical lines.
12.5 cm
3. Divide horizontal lines into required number of equal parts ( depend upon length to measured or read up to)
according to given data for above example maximum length or read up to is 5 m, hence divide parallel lines into 5 equal parts.
Size of individual part = 12.5/5 = 2.5 cm
2.5 cm
2.5 cm
4. Mark ‘zero’ at the end of first division.
0
1
2
3
4
5. Sub-divide only first main part to the left of zero into the required number of sub-division according to unit. In above problem given units are
meter and decimeter and 1 meter = 10 decimeter hence we have to divide first main part into 10 number of equal parts.
Size of individual sub part = 2.5/10 = 0.25 cm
6. Sub-divisions are numbered to the right, starting from zero.
1
2
3
4
5
6
7
8
9
10
7. Assign units for parts.
meter
decimeter
8. Mark given distance on scale. For above problem distance = 3.4 m
3.4 m
9. Name of the scale and R.F. should be mentioned below scale
PLANE SCALE
R.F. = 1 : 40

## Slide 45
Problem 2 :
Construct a plain scale to show meters when 1 centimeter represents 4 meters and long enough to measure up to 60 meters. Find the R.F. and mark on it a distance of 43 meters.
Given data : R.F. = 1 cm is to 4 meters , maximum length = 60 m
Units : meter and centimeter
R.F.
1 cm
4 m
=
=
1 cm
4 X 100 cm
=
1 cm
400 cm
1
400
=
1. Calculate the length of scale.
length of scale = R.F X length to measured
= 1/400 X 60 m
= 0.15 m
= 0.15 X 100 = 15 cm
2. Draw two horizontal lines of 15 cm parallel to each other and
3 cm distance apart. Join the ends by vertical lines.
3. Divide horizontal lines into required number of equal parts ( depend upon length to measured or read up to)
according to given data for above example maximum length or read up to is 60 m, hence divide parallel lines into 6 equal parts.
Size of individual part = 15/6 = 2.5 cm
0
10
20
30
40
50
1
2
3
4
5
6
7
8
9
10
4. Sub-divide only first main part to the left of zero into the 10 number of sub-division.
meter
meters
43 m
PLANE SCALE
R.F. = 1 : 400

## Slide 46
Problem 3 :
Construct a plain scale with R.F. 1:8 to show feet and inches and long enough to measure up to 4 feet, show a distance of 3 feet and 7 inches on your scale.
Given data : R.F. = 1/8 , maximum length = 4 feet
1. Calculate the length of scale.
length of scale = R.F X length to measured
= 1/8 X 4 feet = 1/8 X 4 X 12 inches
= 6 inches
= 6 X 2.54 cm
= 15.24 cm
2. Draw two horizontal lines of 15.24 cm parallel to each other and
3 cm distance apart. Join the ends by vertical lines.
3. Divide horizontal lines into required number of equal parts ( depend upon length to measured or read up to)
according to given data for above example maximum length or read up to is 4 feet, hence divide parallel lines into 4 equal parts.
Size of individual part = 15.2/4 = 3.8 cm
4. Sub-divide only first main part to the left of zero into the 12 number of sub-division. In above problem given units are
feet and inches and 1 feet = 12 inches hence we have to divide first main part into 12 number of equal parts.
Size of individual sub part = 3.8/12 = 0.32 cm
feet
inches
3 feet 7 inches
PLANE SCALE
R.F. = 1 : 8
0
1
2
3
1
2
3
4
5
6
7
8
9
10
11
12

## Slide 47
Problem 4 :
Construct a plain scale with R.F. 1:40 and maximum length is 4 meters. Mark 2.7 m on scale where units are in meters and decimeters.
Given data : R.F. = 1/40 , maximum length = 5 m
Problem 5 :
Construct a plain scale with R.F. 1:50000 to show kilometers and hectometers and long enough to measure up to 7 kilometers. Measure a distance of 46 hectometers on your scale.
Given data : R.F. = 1/50000 , maximum length = 7 km

## Slide 48: Diagonal Scale
Diagonal scale is used in engineering to read lengths with higher accuracy as it represents into three different unit for example meters, centimeters and millimeters.
When measurements are required up to two decimal place (i.e. 3 unit)
Example : 6.71 , 7.34
7.34 m
7 m & 3 dm & 4 cm
For constructing diagonal scale we must know:
Its representative fraction i.e. (R.F.) (given or calculate)
Maximum length to be measured (given)
The units to be shown, for example, milimeters and centimeters(given)

## Slide 49
Steps for constructing diagonal scale
1. Calculate the length of scale.
length of scale = R.F X length to measured
2. Draw two horizontal lines parallel to each other and some distance apart so that they give appearance as a rule. Join the ends by vertical lines.
(1. Length for horizontal parallel lines = length of scale which is calculated previously 2. assume suitable length)
3. Divide horizontal lines into required number of equal parts and ( depend upon length to measured or read upto)
4. draw perpendicular lines at these division points.
5. Mark ‘zero’ at the end of first division.
0
1
2
3
4
6. sub-divide only first main part to the left of zero into the required number of sub-division according to unit.
Unit 2
Unit 1
1 m = 10 decimeter
Hence we need to divide first part into 10 equal numbers
7. Sub-divisions are numbered to the right, starting from zero.
1
2
3
10
8. Mark the given distance on scale
9. name of the scale and R.F. should be mentioned below scale
Diagonal scale
R.F. =
Mark Distance ?
Unit 3 ????
Principle for diagonal scale :
After 7 th step we need to perform few different steps to show 3 rd unit

## Slide 50
Principle for diagonal scale :
z
y
1. Let the XY in figure be a subunit
X
3. Draw parallel lines to XY from all these divisions and number
them 1’, 2’ and so on.
1
2
3
4
5
6
7
8
9
10
0
3’
2’
1’
4’
5’
8’
7’
6’
9’
10’
4. From geometry we know that similar triangles have their
like sides proportional.
In ΔABC and ΔAPQ, ∠PAQ is common and ∠APQ = ∠ABC (corresponding angles)
⇒ ΔABC ~ ΔAPQ (AA criterion for similar triangles)
⇒ AP/AB = PQ/BC
5. Consider two similar triangles XYZ and 7’7Z.
2. From Y draw a perpendicular YZ to a suitable height. 10
Join XZ. Divide YZ in to 10 equal parts.
7Z
YZ
=
7’7
XY
7
10
=
7’7
x
XY
7Z = 7 AND YZ = 10
7
10
=
7’7
x
XY
0.7 X XY
=
7’7
6. Similarly 1’ – 1 = 0.1 XY , 2’ – 2 = 0.2 XY
Thus, it is very clear that, the sides of small triangles, which are parallel to divided lines, become progressively shorter in length by 0.1 XY.

## Slide 51
20 cm
0
1
2
3
1
2
3
4
5
6
7
8
9
10
0
0
1
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
METER
DECIMETER
CENTIMETER
Example : 3.48 m means 3 meter and 6 decimeter AND 8 centimeter
3.68m
DIAGONAL SCALE
R.F. =

## Slide 52
Problem 1 :
Construct a diagonal scale of 1:50 to read meters, decimeters and centimeters to measure upto 5 meters. Show the length of 2 meters, 6 decimeters and 5 centimeters on the scale
Given data : R.F. = 1/50 , maximum length = 5 m and mark 2.65 m
Problem 2 :
On a drawing, a line 10 cm long represents a distance of 5 m. Construct a diagonal scale to read upto 6 m, showing meters ,decimeters and centimeters. Indicate on your scale the length 4.57 m
length of scale = R.F X length to measured
= 1/50 X 5 m
= 0.1 m
= 0.1 X 100 = 10 cm
Given data : R.F. = 10 cm /5 m , maximum length = 6 m and mark 4.57 m
length of scale = R.F X length to measured
= 1/50 X 6 m
= 0.02 X 6 m
= 0.12 m = 0.12 X 100 cm = 12 cm
Problem 3 :
Construct a diagonal scale with R.F. = 1/2000000 to measure upto 300 KM. show on the scale the distance of 236 KM
R.F.
10 cm
5 m
=
=
10 cm
5 X 100 cm
=
10 cm
500 cm
10
500
=
1
50
=
R.F.
1
20,00,000
=
X
300 KM
=
1
20,00,000
X
300 X 100000 CM
=
30
2
15 cm
=

## Slide 53
10 cm
0
1
2
3
1
2
3
4
5
6
7
8
9
10
0
0
1
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
METER
DECIMETER
CENTIMETER
Example : 2.65 m means 2 meter and 6 decimeter AND 5 centimeter
2.65m
DIAGONAL SCALE
R.F. = 1:50
4

## Slide 54
Problem 4 :
Construct a diagonal scale with R.F. 1:24 to show yards, feet and inches and long enough to measure up to 4 yards, show a distance of 1 yard and 2 feet and 4 inches on your scale.
Given data : R.F. = 1/24 , maximum length = 4 yards
Convert 4 yards into CM
4 yards X 3 ( 1 feet = 3 yards)
12 feet X 12 ( 1 feet = 12 inches)
144 inches X 2.54 cm ( 1 inch = 2.54 cm)
365.76 cm
Hence 4 yards = 365.76 cm
length of scale = R.F X length to measured
= 1/24 X 365.76
= 15.24 cm